## Slide 1: PUSHING EXOPLANET DETECTION CAPABILITY USING TUNABLE KERNEL-NULLING
Vincent Foriel1*, Frantz Martinache1, David Mary1
Marc-Antoine Martinod1, Nick Cvetojevic1, Romain Laugier2
1 Université Côte d'Azur, Observatoire de la Côte d'Azur, CNRS, Laboratoire Lagrange, France
2 KU Leuven university, Leuven, Belgium * vincent.foriel@oca.eu

## Slide 2: Nulling Interferometry
Vincent Foriel – WITSO 2025
📚 Bracewell et al. (1978)
Null Depth:
Demonstrated on sky at 📚 Norris et al. (2019)
Require extreme phase stability
📚 D. Rouan (2022)
Notes: Success of such approch rely on extreme phase stability Not the case for 2 reasons (upstream + intrasic)
Null Depth always contain starlight leakage -> hard to distinguish planet signal
To reduce upstream phase sensitivity & have a more robust observable -> Kernel-Nulling

## Slide 3: Noise sources
Upstream AO, fringe tracking
Intrinsic calibration
Vincent Foriel – LIFE 2025

## Slide 4: Kernel-Nulling
Intensity difference between two symetric phase quadrature combinations
Self-calibrated observable
Showing phase closure characteristics
  Robust to first order phase aberration
  Anti-symetric transmission map
📚 Martinache & Ireland (2018)
Vincent Foriel – LIFE 2025
Notes: KN can be built with more telescopes to be even more efficient
Too much telescopes, the complexity become crazy

## Slide 5: Photonic technology
Vincent Foriel – LIFE 2025
Photonic chip made of SiN ( large)
H band ()
Notes: Derived from network and telecommunication (Can operate in 1.65μm --- 1.55 is more affordable)
Photonic still have intrasic phase aberration (manufacturing defects)
Chip has active elements -> tunable architecture

## Slide 6: Multi Mode Interferometer (MMI)
Wave propagation simulation in a MMI (Multi Mode Interferometer) 📚 N. Cvetojevic et al. (2022)
Vincent Foriel – LIFE 2025
Variation of the beam splitting ratio at the outputs of the 4x4 MMI 📚 P. Chingaipe (2024)

## Slide 7: Tunable architecture
Vincent Foriel – LIFE 2025
Thermo-optic phase shifters
W for phase shift
ms time response
Notes: Thermo-optic phase shifter – 0,6W for
We decomposed the overall interferometric operation into series of 2x2 MMI
To control the phase at each elementary step of the process
Compensate for intrinsic phase aberration
14-dimension parameter space -> need to be calibrated

## Slide 8: Two calibration approaches
Vincent Foriel – LIFE 2025
Trial & Error
Add a shift somewhere
Look at the output
Is it better?
Yes: Keep it No: Reject it
Repeat
Obstruction
Isolate one MMI
Tweak input relative phase
Deduce right shift from output response
Do it for all MMI
Notes: Thermo-optic phase shifter – 0,6W for
We decomposed the overall interferometric operation into series of 2x2 MMI
To control the phase at each elementary step of the process
Compensate for intrinsic phase aberration
14-dimension parameter space -> need to be calibrated

## Slide 9: Comparison
?
Trial & Error
Trial & Error fit
Obstruction
Obstruction fit
Ideal
Trial & Error
Obstruction
?
Vincent Foriel – LIFE 2025

## Slide 10: Specific statistical test
Vincent Foriel – LIFE 2025

## Slide 11: Detection capability
VLTI conditions: up to
  Performances mainly limited by atmosphere
  In accordance with the literature 📚 Norris et al. (2019)
LIFE conditions: up to
  Possible exo-earth detection
  Missing perturbation sources in the numercial model?
⚠️ Numerical simulations
  Soon to be validated in lab
VLTI LIFE
SAO model of our solar system 📚 Kaltenegger et al. (2010)
Vincent Foriel – LIFE 2025

## Slide 12: Conclusion
Compact, stable, light
Possibility to make it almost ideal
VLTI ASGARD/NOTT
LIFE
Future prospects
Vincent Foriel – LIFE 2025
Notes: Conclusion (miniaturization, stability, performance)

## Slide 13: Thank you!
vincent.foriel@oca.eu

## Slide 14: Backup slide Obstruction approach
Isolate a single MMI
Scan on one shifter
Fit output response
Introduction / Materials / Calibration / Results / Conclusion
Vincent Foriel – LIFE 2025

## Slide 15: Backup slide Trial & Error approach
 |  |  | … | 
 |  |  | … | 
 |  |  | … | 
 |  |  | … | 
👎
 |  |  | … | 
 |  |  | … | 
👍
👌
 |  |  | … | 
 |  |  | … | 
Initial
Step 1
Step 2
Final
…
Null Depth should be minimized
Measurement
Introduction / Materials / Calibration / Results / Conclusion
❌
✔️
Vincent Foriel – LIFE 2025

## Slide 16: Backup slide Kernel-Nulling
📚 Martinache & Ireland (2018)
🔎 Why is it more robust?
An output intensity is a combination of the input fields
If we introduce small perturbations on these fields
We can then express a pair of output intensity such as
By simplifying, we obtain
So
📚 Martinache & Ireland (2018)
For , such as

## Slide 17: Backup slide MMI: Multi Mode Interferometer
🔎 How does it work?
A single-mode light entering a multimode region will excite several transverse modes that will interfere. These interferences will produce an image of the input at specific positions: , , , ...
Wave propagation simulation in a MMI cavity 📚 Cvetojevic et al. (2022)
Self-imaging multi mode waveguide
Operation defined by the length
🤔 What is a mode?
In a waveguide (fiber optics), the light doesn’t propagate freely, it is constrained between the borders. Like a guitar string that vibrates when pinched on both sides, the light wave can only take specific shapes that respect theses constraints.
Monomode fiber
Multimode fiber

## Slide 18: Backup slide Thermo-optic phase shifters
Response time ~ 1 μs
Phase range > 2λ
Recipe:
Electric resistance
⤷ Heat
⤷ Optical index modification
⤷ Phase delay
🔎 What’s the physics behind?
In a material, the light speed is defined such as
The refractive index is related to the material’s polarizability and its electronic band structure. When the temperature increases:
Thermal vibrations (phonons) increase → atomic bonds become more flexible → the electronic response to an electromagnetic field is modified.
This affects the dielectric permittivity , hence ​ (with for non-magnetic optical materials).
The broadening of electronic transitions or absorption bands can also modify , according to Sellmeier dispersion.
There is no universal exact expression of . However, we empirically use the following linear approximation which is valid for small temperature variation:
Were is the reference temperature (typically ) 📚 Wikipedia

## Slide 19: Backup slide Output data analysis
Kernel outputs follows an unknown distribution
Companions affect this distribution
In practice, SNR << 1
Searching for most efficient specific statistical test